Agriculture Equipment’s and Smart Technology

Utkarsh Dwivedi1*, Apeksha1, Bharath Kumar Komatineni2, Sajesh Chettri1, Amit Gupta1

1College of Agricultural Engineering and Post Harvest Technology, CAU Imphal, Sikkim, India – 737135

2College of Technology and Engineering, MPUAT, Udaipur, Rajasthan, India- 313001

*Corresponding author Email: utkarsh.ud555@gmail.com

ABSTRACT

Agricultural production pf crops involve every aspect of cultivation, harvesting, processing, storage, and transportation are included in. Agricultural inputs including labor, water, arable land, and other resources (such as energy, fertilizer, etc.) are crucial for agricultural productivity and are significantly affected by the type and scope of farming techniques. agriculture production provides locals with considerable employment possibilities, food security, and opportunities for economic growth in many developing nations. To improve crop yields, efficiency, and sustainability, modernization, automatization, precession in agricultural operation is needed. Smart agriculture and precise agriculture are only getting started, but they might pave the way for far larger use of technology in the farming environment. Technological advancement, IoT development, and mobile application have all contributed considerably to the acceptability of technology in agriculture. The employment of computers, software, sensors, and other information technology in smart farming techniques and methodology can be linked to technological advancement. Evidently, smart farming is a creative agricultural approach that, when implemented correctly, may assist farmers in achieving an array of benefits including increased yield, enhanced quality, and lower costs.

INTRODUCTION

Agriculture is one of India's most common occupations. Agriculture products contribute greatly to the national economy. Sowing, planting, irrigation, fertilizer spraying, harvesting, and other traditional agricultural techniques have seen considerable advancements as a result of engineering research. However, in order to further enhance our economic status, we must increase agriculture quality and productivity. Agriculture is now facing a workforce shortage. Farmers prefer to use reaper harvesters due of shortage. These reapers are costly and only available for a large-scale field. (Bhabad et al.2017).

Traditionally, numerous diseases were not detected by farmers due to the absence of information and the lack of a local expert. The integration of digital technologies and focused on the future technologies for usage as smart object are the most basic criteria for agricultural progress. (Keller et al., 2014)

Mechanization is the replacement of mechanical energy for biological energy at different phases of the manufacturing process. In the agricultural sector, mechanization refers to the use of suitable machinery to speed up the completion of field tasks and the proper use of numerous agricultural inputs. In other words, appropriate tools and implements, equipment for agriculture, combines, pumping systems and other equipment are introduced at a proper level. (Sarkar, A. 2020).

Mechanization of farms in India is at 40%-45%, which still appears lower when compared to countries such as the United States (95%), Brazil (75%), and China (57%). Although mechanization lags behind a number of other developed countries, it has made remarkable development in the last decade. Agricultural electricity availability on Indian farms grew from 1.47 kW/ha in 2005-06 to 2.02 kW/ha in 2013-14. (Anonymous 2014).

Farm Management Systems (FMSs) are critical for achieving advanced operational farm management because they include features for planning, coordinating, monitoring, and regulating agricultural activities.

However, present FMSs typically depend on specific models, and their functions do not go beyond agricultural data monitoring and the distribution of selected control services via standalone applications that are tightly associated with each system because they consist of closed specifications for commercial infrastructures and address specifically selected clients. This imposes major limits on the FMSs' interoperability as well as the semantic labeling of the myriad varied agricultural data that they must handle. FMSs should be capable of improving the performance of these tasks in the area of sustainability.

- At reduced costs, carry out efficient and interactive automated agricultural activities (such as cultivation, monitoring, irrigation, and so on) in complicated surroundings and farm structures.

- Ensure effective and secure working circumstances for the environment as well as agricultural stakeholders (such as farmers, agronomic engineers, policymakers, development cooperation experts, and so on).

- Increase synergies among all agricultural stakeholders, allowing them to make choices on issues that are outside their areas of competence.

These goals can be met by promoting a comprehensive approach to from end-to-end farm management, which is based on the coordinated internal and external relationship of technologies as well as farming infrastructures, processes, and applications in an intelligent digitalized the surroundings, in the context of Agriculture's cutting-edge trend. 4.0

Furthermore, data-driven farm management might be used to alleviate production issues. To boost efficiency, data management is required for data/information analysis. This technique illustrates how robots are going to play a major role in farming's future growth. (Saiz-Rubio & Rovira-Ma´s, 2020)

According to the standard definition, precision agriculture is "the use of current technological innovations to provide, process, and evaluate multi-source data of high regional and temporal resolution for the purpose of making decisions and operations in farming and crop management." This precision agriculture may result in increased yields of crops, soil degradation, enhanced water use, a reduction in the volume of chemical pesticides and fertilizers used in cultivation, and the adoption of modern farming practices that enhance crop quality, quantity, and cost. The purpose of incorporating Agriculture IoT solutions is to aid farmers in bridging the supply-demand mismatch, which may be done by ensuring high yields, increasing earnings, and protecting the environment.

Precision agriculture refers to techniques that leverage Internet of Things (IoT) technology to ensure effective use of existing resources, with the objective of boosting agricultural output while decreasing operational costs. The Internet of Things has a multitude of applications in precision agriculture, but the most significant among them are crop sowing, crop management of water, management and controlling of insects, precise detection and nutrients management, yield monitoring, and safe storage management. All of the measurements may be obtained using sensors, and the data is subsequently stored in the cloud or on a server connected to the network for further processing, as shown in Figure 1. The modification of sensors over time highlights the advances achieved in the measurement of a wide range of characteristics, which includes temperature, pH, humidity, and analytical data like potassium, phosphorous, and nitrogen readings from a remote site. Temperature, pH, and humidity are examples of all of these variables.

Fig. 1: Historical progression of sensor

Agriculture contributes significantly to India's total economy. More than 70% of the rural population relies solely on agricultural earnings for financial security. It employs more than 60 percent of the entire population and provides around 17 percent of the country's overall gross domestic output. Over the last several decades, India's agricultural sector has grown at an astounding rate. On the other hand, the reality is that a lot of farmers in India are committing suicide which is quite concerning. Farmers gave them the following reasons for taking their own lives, in order of importance: financial obligations, environment, low food prices, bad irrigation, increased agricultural expenditures, the usage of chemical fertilizers, and failure of crops.

Intuition and other irrelevant problems, such as the need to provide immediate earnings, a lack of demand from the market knowledge, overestimating a soil's capacity for sustaining a particular crop, and so on, have a tendency to cover up a farmer's decision of which crop to grow. This makes the decision challenging for the farmer to choose. An important task that must be completed as soon as possible is the development of a system that can offer Indian farmers with predictive insights and assist them in making accurate choices about what and how to cultivate in order to increase production.

This project must be completed as soon as possible. As a result, there is a growing demand for "smart farming," which is made possible by the Internet of Things (IoT). The application of Internet of Things (IoT) technology in agriculture has the potential to alter not just the lives of people but also the entire environment. By examining sensor data, farming operations become more transparent, allowing farmers to get critical insights about the well-being of their crops, greenhouses for cultivation, and other facilities. Farming driven by machine learning and employing high-accuracy algorithms is a revolutionary concept that is gaining favour in today's culture. This unique effort makes sustainable product development feasible for everyone involved in the agriculture business. This movement aims to boost both the number and quality of farm goods already cultivated in the fields.

Precision farming and land management, as well as scientific findings from observation of the earth and climate change research, and cutting-edge technologies such as image processing, geographic information systems (GIS), and unmanned aerial vehicles (UAVs), would all help to improve the production of agricultural goods. Farmers may get crop and market information through digital agriculture, which uses information and communication technologies. (Costa et al., 2011).

Geo Farmer is a project tracking and feedback platform for agricultural innovation. Farmers can better manage their crops and farms if they communicate their positive and negative experiences with one another as well as with professionals (Eitzinger et al., 2019). As shown in Fig. 2, the traditional way of agricultural farming may be changed into smart agriculture by making the necessary modifications to the current method.

Fig. 2. The transformation of traditional agriculture to smart agriculture practice

Unfortunately, farmers who are still far away from modern innovations and rely on traditional agricultural and food supply systems have a low rate of productivity, and different countries produce yields that are much lower than their potential (Kumar & Ilango, 2018). Modern technology can play a critical part in overcoming these issues and bringing about a revolution in the agricultural industry. (Timalsina, 2019).

Smart Technologies Available in Agricultural Fields

Agricultural Internet of Things (AIoT)

The Internet of Things (IoT) may be described semantically as a global network of uniquely addressable things that are linked together using standard communication protocols such as Internet. As a result, the Internet functions as a storage and communication infrastructure, with virtual object representations that merge pertinent information with actual items. In this context, virtual objects act as centralized object information hubs, constantly updating and merging data from a variety of sources in order to operate any needed activities remotely over the Internet. (Botta et al. 2016)

Physical and virtual items are interconnected and inter-controlled by intelligent networks developed along the whole value chain, according to the criteria of Industry 4.0 in general and Agriculture 4.0 in particular. Based on this concept, the virtual object structure is inextricably linked to the IoT concept, which in both the agricultural and industrial sectors can be expressed by specific features such as heterogeneity due to a wide range of devices, interconnectivity, high adaptability, object-related services, and, finally, dynamic changes because device status can change dynamically at any time. (Lakhwani et al. 2018)

According to Agriculture 4.0 guidelines, the Agricultural IoT (AIoT) indicates to a promising structure through which many factors of farm data can be acquired, processed, managed, and transmitted as a mechanism by using which a diverse series of systems and services can be seamlessly integrated within FMSs. (Ma J et al. 2012). Such systems will be able to:

- Handle the ever-increasing diversity of real-time data streams successfully;

- Handle a variety of data that is incomplete and, in some situations, conflicting;

- Real-time data acquisition, correlation, and fusion

- Change network behavior dynamically to vary data gathering,

- Embrace distributed intelligence and multi-agent approaches to facilitate organized sensing activity by allowing individual network nodes to reason, operate, and collaborate within a collective structure, recognizing the concurrent existence of both individual and a joint objective.

As a result, the AIoT is regarded as a must-have technology for smart farms, and its advancement in relation to the Future Internet approach provides a foundation for a new generation of Farm Management Information Systems, allowing whole smart farms to develop into active nodes in the value chain of agriculture.

3.4. Artificial Intelligence (AI) and Machine Learning (ML)

Agriculture confronts several obstacles due to uncertainty in different activities such as seed sowing, pesticide control, weed management, crop disease infestations, a shortage of irrigation and drainage infrastructure, and even a lack of control over storage. Artificial Intelligence (AI) and Machine Learning (ML) techniques give inteligent software applications and systems capable of performing knowledge-based functions involving subtle judgments and unorganized commands in order to enable efficient risk management, minimize prediction costs on taking decisions, and, as a result, improve intelligent agricultural accuracy as well as efficiency. Patrício and Rieder 2018.

To acquire the correct content value for heterogeneous data in agricultural situations, numerous data abstraction layers and multiple feature selection approaches, such as clustering and classification, are necessary. Data fusion methods for classification, in particular, can be widely applied in multisensory environments with the goal of fusing and aggregating data from multiple supplied heterogeneous sensors (such as those used in agricultural farms) to achieve lower detection error probability and higher reliability. FMSs can use a variety of AI-based approaches for this goal, including Artificial Neural Networks (ANNs), C5.0 techniques for classification, Bayesian fusion, and Hidden Markov Model (HMM) methods, as well as unsupervised learning methods in some circumstances. Furthermore, as an exploratory data analysis tool, clustering is commonly used for discovering subgroups (clusters) in data based on the similarity or variety of data points. Furthermore, by utilizing ML approaches, FMSs can mature into true AI systems, delivering more advanced insights and suggestions for any following decisions and activities, eventually striving to increase agricultural productivity. In this regard, it is expected that the incorporation of ML models in FMSs will develop even further in shortly through the integration of automated information recording, data analysis, ML implementation, and taking decisions or support, providing practical tools that align with the agriculture 4.0 guidelines to raise the production and quality of agricultural produce in terms of sustainability. Dahikar and Rode 2014)

Agricultural Robotic and Autonomous Systems

Robotics and autonomous systems are inherently complicated in that they are composed of several subsystems that must be connected and correctly coordinated in order to perform duties flawlessly as a whole and successfully distribute any essential information. This type of integration is critical for accounting cycle durations and time delays, as well as communication characteristics across all subsystems [45]. Agricultural Robotic and Autonomous Systems, which perform various field tasks which include sowing, trimming, phenotyping, targeted fertilization, harvesting, and sorting in automatic or near to automatic modes, are even more complicated and sophisticated because they must operate in unstructured agricultural conditions in order to reduce farmer workload, boost production rates, advance soil health as well as the quality of yields, and accomplish the management of resources. (Reiser et al. 2019)

The major challenges that must be addressed in order to effectively incorporate robotic technology into agricultural operations:

- Problems such as the constantly changing conditions and variability of agriculture's output and environment, as well as challenging circumstances (i.e. dust, vibration, extreme temperature, and also humidity), must be overcome through advancements in adequate equipment and intelligent mechanisms in order to achieve a successful outcome.

- The expenses of robotic systems must be considered in FMSs in order to actualize the practical use of various types of robots and expand their penetration into the agricultural sector. In this regard, because agricultural products are generally low in value, the costs of robotic systems must be sufficiently reduced to economically justify their use.

- To be fit for functioning unattended in open fields, autonomous systems must overcome inherent safety and dependability challenges, as safeguarding persons, the environment, crops, and machinery is still required today.

Role of image processing in agriculture

Image processing in agriculture is a significant step toward agricultural modernisation. Image processing is a technique for enhancing an image or extracting usable information from it. Image processing is an established technology in agriculture for increasing output rates and meeting global agricultural demands. Image processing using various spectrum measurements, such as infrared and hyperspectral X-ray imaging is useful in diagnosing agricultural illnesses, weeds, and land mapping, which may help farmers save money and time. Detecting crop illnesses can assist farmers in dealing with infections and preventing them from spreading to the overall output. Imparting image-processing technology in modern agriculture will boost agricultural productivity to meet market demands and deliver timely updates to farmers via numerous automated applications in agriculture. The paragraph that follows explains and examines the various specialized uses of image processing in the agriculture sector. (Feng et al., 2018)

3.1 Plant disease identification

Image processing is commonly utilized for identifying plant diseases in a variety of agricultural crops. Farmers confront significant dangers as a result of the growth of numerous pests and diseases in crops. Some of the most prevalent causes of illness infections are fungi, bacteria, viruses, and nematodes. Most infections were previously not identified or suspected by farmers because they lacked understanding about crop diseases and needed assistance and advice from professionals. However, early detection of diseases can help to reduce crop loss. Image processing is vital for identifying plant diseases since disease identification and detection are only possible with visual information. For disease identification and analysis, a neural network-based technique is proposed (Jhuria et al., 2013).

The diagnostic strategy is presented to identify the disease using an intelligent system. The work is done on apple and grape plantations. The system made use of two separate databases. The authors established a study on illness categorization and mapping according to color, texture, and morphology. The writers received better findings, and grading was completed. The grading will assist farmers in determining the amount of pesticide needed. Further studies (Chahal & Anuradha, 2015) proposed a system for plant disease categorization and identification of plant and leaf disease.

In addition, the authors suggested a wide paradigm for image processing. Support vector machines (SVMs), neural networks with k-means, and principal component analysis (PCA) were among the effective categorization algorithms studied. Using image processing technology, several researchers developed a variable-rate chemical application system.  The primary goal of the project was to discover diseases on rice crops. To detect the unhealthy zone of rice plants, an image segmentation approach based on chromatic aberration was applied. The author created a prototype that consumes fewer chemicals and has a diagnostic technique for variable rate application. This strategy is both environmentally and economically advantageous (Tewari et al., 2020).

3.2 Fruit sorting and classification

As day-to-day activities boosted consumer demand, many fruits were supplied in marketplaces for consumption. These fruits are sorted out by hand which is a biased, time-consuming, and exhausting procedure because vast amounts of fruits must be sorted out in a short period of time (Butz et al 2006). Image processing mixed with other approaches can be utilized as expert advise to improve output, according to researchers (Surya & Satheesh, 2014). The suggested model categorizes and displays image processing applications in agriculture, and it presents a framework for future research in image processing. These strategies aid in the creation of the automation model and the acquisition of more accurate information.

Automatic sorting and classification of fruits is a postharvest process where the application of image processing is introduced for automation.

This method is more advantageous than human labor with more accuracy, reliability, speed, and consistency. The industrial sector is benefited by the automated sorting of fruits and vegetables by applying this non-destructive method of classification (Bogue, 2016). Fruits with different size, color, shape, and texture can be easily identified and separated. Damaged fruits and vegetables can also be easily identified and removed. This automation helps the industries, supermarket stores, and other wholesale fruit stores to sort the fruits in a shorter period with high accuracy.

3.3 Plant species identification

Plant species identification is another helpful use for botanists, researchers, and even the average person. In the identification of species from a collection of species photos, content-based image retrieval is utilized. Plants are distinguished by morphological traits such as the texture, size, form, and color of their leaves and flowers. For species identification, the assistance of a skilled and knowledgeable botanist is required. Information technology, such as real-time picture capture equipment, can be used to solve this problem. The extraction of features and analysis of images are critical components in identifying plant species from a collection of species photos. According to researchers (Farmer & Jain, 2005), shape analysis on leaves may be done based on the leaf border. Leaf analysis may be divided into two categories: region-based and boundary-based.

Boundary signatures can be used to identify plant species by applying them to the leaf's boundary regions (Femat-Diaz et al., 2011). Other characteristics, such as leaf color and texture, are considered for categorization. When the color feature is paired with the form feature, the accuracy of the findings may be improved.

3.4 Precision farming

The advancement of information technology and agricultural research has enabled the merging of these two industries, resulting in the growth of precision agriculture. This can help farmers make more informed judgments about crop output. It entails good comprehension and efficient exploitation of natural resources available in the field. It provides optimum profit and output with little input and best resource use. Farmers must have prior understanding of technology and how it works. Farmers must be properly trained in order to learn about precision agriculture. Precision agricultural equipment uses the global positioning system (GPS) and geographic information system (GIS). GIS is used to identify all accessible data, while GPS assists in determining the position of an object on the globe via signals from satellites. Images obtained remotely by satellite may be retrieved and analyzed in digital form. Remote sensing, like GIS, has advanced independently due to advances in image processing techniques. To improve precision farming, an integrated system that combines remote sensing equipment and software for image processing is employed.

3.5 Fruit quality analysis

Awareness among consumers and market demand for quality products have resulted in the creation of a quality evaluation automation system. This requires fruit quality inspection in order to have high-quality fruits on the market. Fruit quality is assessed using attributes such as color, shape, flavor, texture, and size (Freixenet et al., 2002). Image capture, processing, and interpretation for analysis are all part of this computer vision activity. Extracting the fruit region from the backdrop became a critical step for examining the primary features to evaluate the fruit quality. The fruits are classified into distinct quality groups. Grading is done using various patterns and classifiers. Color, size, texture, and form are regarded as essential grading characteristics (Mendoza & Aguilera, 2004).

Manual examination takes time, is prejudiced, and prone to mistakes. To address these challenges, a non-destructive quality assessment approach was created that, in contrast to certain destructive procedures, could detect fruit quality with greater precision and speed. Nowadays, computer vision-based automated quality evaluation systems are replacing conventional manual inspection in several sectors (Gao et al., 2010). To rate the quality of fruits, classifiers such as neural networks, SVMs, Bayesian decision theory, k-nearest neighbors (KNN), and PCA can be used. The automated system's quality evaluation decisions have shown to be useful and beneficial to a variety of food businesses. Color, shape, and size are the major criteria to examine when estimating quality (Prabha & Kumar, 2013). Some study as provide critical knowledge as well as a method for generating pea-based, tofu-free soybeans.

3.6 Crop and land assessment

Remote sensing has become one of the most important data sources that are used in GIS for getting information from satellites. The reflection of visible light energy from an external source is a significant aspect in remote sensing. The sun is an external supplier of energy for passive systems. The adoption of image sensors has boosted the amount of information acquired by satellites. Images obtained remotely by satellite may be retrieved and analyzed in digital form. Remote sensing has advanced independently of GIS due to advancements in image processing techniques such as picture enhancement, restoration, and analysis. Remote sensing's primary goal is to monitor the Earth's surface and therefore assess geographical, biological, and physical factors in order to identify the materials on the ground cover for further research.

3.7 Weed recognition

Weeds are a concern to farmers because they affect agricultural yield and quality. As a result, greater effort is required to monitor weeds. Herbicides are one of the most used methods for controlling weed growth. Weed recognition is now controlled automatically so that the system can tell the difference between weeds and crops. The automatic system analyzes weed growth on a regular basis and determines when to control it. Classifiers, in conjunction with image processing approaches, make it simpler to identify and eradicate weeds in their early stages (Lamb & Brown, 2001). Researchers proposed image processing to evaluate agricultural parameters and explaining how image processing for various spectrums, such as infrared and hyperspectral X-ray, may be useful in identifying vegetation indices, canopy estimation, irrigated land map tracking, and other applications. The authors define an image porosity work that includes algorithms for surveying and weed categorization. With the proper imaging methods and algorithms, classification accuracy may reach up to 96%. Image processing was examined by the researchers (Poojith et al., 2014) to identify weeds in the field. The suggested approach captures photos and processes them using MATLAB to identify weed spots in the field. A well-defined algorithm technique may also recognize weeds and spray them with weedicide.

The value of the threshold should be carefully determined for two distinct sorts of weeds. Weedicide consumption may be minimized by using this practice, saving the environment. The huge range of uses for counting items in digital photographs makes it impossible to foresee all possible helpful ideas. Specified a work examining the application of image processing in the agriculture industry, such as imaging approaches for managing crops. Researchers (Prakash et al., 2017) used MATLAB image processing to locate weed patches in field photos, which can lead to viable remedies for serious issues being overlooked. Again, for crop and weed identification and classification, one study (Bosilj et al., 2018) proposed a method based on SVM with the help of attribute morphology that classifies the detected areas into three groups, namely weed, crop, and mixed. The study's findings revealed effective and complete categorization rates. On sugar beets and onions, the proposed approach was applied and assessed.

4 Role of Machine Learning in Agriculture

In modern agriculture, machine learning is a promising technique. ML may be used to spray pesticides, fertilizers, and various other chemicals in agricultural areas using robots. The integration of ML and IoT enables monitoring of a farm's state and estimation of damage severity. By concentrating on the most successful regions, this would reduce fertilizer consumption by 70%. That will be good for both the economy and the planet's health. These ML applications would minimize agricultural waste by 60%, lowering the carbon impact and protecting the environment. This provides farmers with economical and tailored agriculture solutions. With its numerous uses, ML may be used to do tasks such as crop forecast, crop management, and disease diagnosis. Machine learning models have been used in a variety of applications, including crop management, yield prediction, and disease detection (Liakos et al., 2018). The section that follows covers and examines the many specialized uses of ML in the agricultural sector.

4.1 Yield prediction

One of the most important study topics in precision agriculture is yield prediction. To boost productivity, yield estimate, yield mapping, crop supply matching with consumer demand, and crop management are critical. According to previous research an early yield mapping method that identifies premature green citrus in a citrus orchard under open-air environmental conditions was established. This research also assists farmers in optimizing their orchards for better revenues and harvests. Another study offered a methodological technique and created a machine vision system that shakes and captures cherries autonomously during harvesting. In each case, the framework separates and recognizes obstructed cherry branches with foliage, even if they are imperceptible. The framework's goal was to minimize labor needs. (Amatya et al., 2015). In this research they develops a framework for detecting tomatoes using expectation maximization (EM) and remote sensors. The suggested system detects Red, Green, and Blue (RGB) pictures taken by a UAV. The research study (Ali et al., 2016) suggested a model that predicts grassland biomass (in kg dry matter/ha/day) using artificial neural networks (ANNs) and multitemporal remote sensing data. Another study (Pantazi et al., 2016) proposed a satellite imagery-based method. The suggested approach is designed exclusively for predicting wheat production. The system gets crop growth parameters along with soil data, which improves system performance and increases prediction accuracy.

In one study a generalized technique for predicting agricultural yields was developed. The approach is based on the use of an extension neural network (ENN) to long-term agronomical data (1997-2014). The research was a regional forecast, focusing on Taiwan. The research helps farmers maintain market supply, demand, and quality of crops. (Kung et al., 2016), Another study revealed an efficient, non-destructive, and cost-effective technique for counting fruits, in this case, coffee on a branch. The suggested approach divides coffee fruits into three categories: non-harvestable, harvestable, and fruits with an unknown maturity stage. This approach assists coffee producers in planning their work and maximizing economic rewards. (Ramos et al., 2017) Other researchers established a model for rice development stage prediction based on SVM and basic geographical data obtained from a meteorological station in China. (Ying-xue et al., 2017). Another work developed the ML technique for predicting crop output and estimating nitrogen status. A proposed strategy involves merging ML with other technologies to create a hybrid system for cost-effective and compressive agricultural solutions.

Finally, major advances in sensing, techniques, and machine learning will allow for more cost-effective and compressive solutions for enhanced crop and environmental condition estimations. One study (Murugesan et al., 2019) described work on ML on three platforms, including Python, R, and Seaborn, for soil management. A prototype of an unmanned ground vehicle (UGV) was also created to gather soil properties and anticipate agricultural production (Aravind et al., 2017).

One study used a unique strategy to food research that might make a significant contribution to expedited screening of food and brewing products for the food sector as well as the application of artificial intelligence (AI). Robo BEER has proved to be an effective, unbiased, exact, and time-saving technique for anticipating sensory descriptors in comparison to expert sensory panels. This method might potentially be used as a quick screening procedure to determine the consistency of beer at the end of the manufacturing process for industrial purposes. (Gonzalez Viejo et al., 2018).

4.2 Disease detection

The most widely used approach in irritation and disease control is to spray pesticides over the cropping area on a regular basis. This approach, even though it is effective, comes at a great financial and environmental cost. ML is a coordinated component of precision agriculture management in which agro-synthetic compound input is targeted in terms of time and location. One research provided a systematic technique for distinguishing between healthy and yellow rust-infected wheat using an ANN model and spectral reflectance data. Based on a self-organizing map (SOM) neural network and data fusion of hyperspectral reflection and multispectral fluorescence imaging, a real-time remote sensing model developed identifies yellow rust-infected or healthy wheat. (Moshou et al., 2005). In terms of water-stressed Septoria trici, researchers (Moshou et al., 2013) suggested a method that automatically distinguishes between healthy and diseased winter wheat canopies. The proposed classifier is based on least square (LS)-SVM and multisensory optical fusion. A further study (Chung et al., 2016) proposed a technique for identifying and screening Bakanae disease during rice seedling. The study's major goal was to improve the detection of the disease, Fusarium fujikuroi, in two rice varieties. The proposed approach saves time while increasing grain production. Wheat crops were likewise subjected to the same automated detection system.

Other researchers suggested a technique for identifying and distinguishing between healthy Silybum marianum plants and those infected with the smut fungus Microbotyum silybum. Another work (Pantazi et al., 2017) developed a system based on a hierarchical self-organizing classifier using hyperspectral reflectance image data that recognizes nitrogen-stressed and healthy winter canopy as well as yellow rust-infected canopy. The study's major goal was to obtain useful fertilizer and fungicide usages based on plant requirements. 4.3 Weed identification It is also one of the earliest agricultural challenges. Weed identification and differentiation from crops is quite challenging.

ML algorithms can be a beneficial tool when used with sensors to improve detection and classification, reducing the need for herbicides. One study (Pantazi et al., 2016) provided a methodological technique and created a model for recognizing crop and weed species. The suggested approach is built on machine learning and hyperspectral imaging. The study's major goal is to identify and distinguish different forms of maize (Zea mays) as an agricultural crop and Tarraxacum officinale, Ranunculus repens, , and Urtica dioicaas as weed varieties.

Based on counter propagation (CP)-ANN, one study (Pantazi et al., 2017a) developed a technique for identifying Silybum marianum using multispectral images obtained by unmanned aircraft systems. This weed significantly reduces agricultural output and is extremely difficult to identify.

4.4 Crop quality

It is critical to identify crop quality characteristics in order to improve product pricing and decrease waste. Researchers (Maione et al., 2016) proposed a method for predicting and identifying the geographic location of rice samples based on ML methods utilized in sample chemical composition. The study's findings revealed that Rb, K, Cd, and Mg are the most important chemical components for sample categorization. One study (Zhang et al., 2017) provided a methodological technique and built a model that identifies and categorizes botanical and nonbotanical foreign materials contained in cotton lint while harvesting. The study's major goal was to increase quality by avoiding fiber damage. Another study (Hu et al., 2017) looked at the ML approach combined with hyperspectral reflectance imaging to detect and categorize Korla fragrant pear into deciduous-calyx and persistent-calyx classifications.

4.5 Species recognition

The researchers (Jha et al., 2019) offered techniques for agricultural automation activities such as IoT, wireless communication, machine learning, artificial intelligence, and deep learning. Automation is the key to increasing output and improving soil fertility. The suggested method is for identifying leaves and flowers as well as watering plants.

4.6 Soil management

ML is used to forecast and detect agricultural soil parameters such as soil conditions, temperature, soil dryness, and moisture content. (Coopersmith et al., 2014) suggested a technique for evaluating soil dryness using evapotranspiration and forecast data from Urbana, Illinois, in the United States, to aid in agricultural planning. The suggested method's major goal was to provide remote farm management choices.  (Morellos et al., 2016) provided a methodological technique and produced a model that forecasts soil conditions in one investigation. The author used a Vis-NIR spectrophotometer to gather soil spectra from 140 raw and wet extracts of the top layer of various Luvisol soil types for the investigation. in August 2013, the samples were taken from an agricultural field near Premslin, Germany. A model based on a selfadaptive evolutionary extreme learning machine (SAE-ELM) with meteorological data was given in one paper (Nahvi et al., 2016). Daily soil temperature was estimated at six distinct depths in the study, namely 5, 10, 20, 30, 50, and 100 cm, in the two distinct climate condition areas of Iran: Bandar Abbas and Kerman. A third research (Johann et al., 2016) offered a unique approach for estimating soil moisture that relied mostly on the ANN model and a dataset from force sensors mounted on a no-till chisel opener.

5.4 Crop type classification

Kusul et al. (2017) developed an approach for classifying crops such as wheat, soybean, maize, sugar beet, and sunflower. The study makes use of a database that contains 19 multitemporal scenes taken by Landsat-8 and Sentinel-1A RS satellites from a Ukrainian test site. The suggested technique has an overall classification accuracy of 94.60%, which is higher than the RF (88%) and multilayer perception (MLP) (92.7%). Another work (Ghosal et al., 2018) looked at a deep machine vision-based approach for identifying, classifying, and measuring plant stressors, both abiotic and biotic, utilizing a library of 25,000 photos of healthy and stressed leaflets in the field. The Deep CNN model achieves a classification rate of 94.13%.

5.7 Crop yield estimation

Researchers (Kuwata & Shibasaki, 2015) reported a study using CaffeNet for estimating maize yield with a root mean square error of 6.298, which is better than support vector regression (8.204). The dataset was acquired from the climate research unit, and it included maize yield data from 2001 to 2010 using a moderate resolution image spectroradiometer improved vegetation index. Another research (Kamilaris & Prenafeta-Boldu', 2018) characterized work on a CNN and discussed its benefits and drawbacks. This method is for implementing CNN in a sugarcane farm in Costa Rica, and the future potential of DL is also explored in other regions.

5.8 Fruit counting

Picture segmentation and object identification are presently dominated by DL-based approaches (Badrinarayanan et al., 2017). The large amount of data utilized for training, from which the networks gain traits that ideally generalize across circumstances, is widely attributed with these technologies' overwhelming success. Previously, the fruits count was dominated by the circular Hough transformation (CHT) (Pedersen & Kjeldgaard, 2007). CHT requires significant parameter tweaking and is unable to handle occlusions. These difficulties inspired the creation of more complicated fruit-counting systems.

Based on DL, one study proposed a data-driven strategy for counting oranges and apples. They began by introducing a labeling platform for classifying the fruits on input image files. The candidate region was then extracted using a blob detection neural network. Another neuron is used to count the number of fruits in the image once more. Finally, regression analysis is used to compare the performance of algorithmic and manual counts. This approach is applied to oranges and apples with the intersection of union (IoU) values of 0.813 and 0.838, respectively.(Hani et al., 2018) looked at the issue of reliably counting fruits from photographs. They demonstrated a system that makes use of AlexNet CNN to modify and fine-tune the data they use for training. The approach attained an accuracy of 80% to 94%. Fruit detection and counting gained popularity with the introduction of faster R-CNN. Researchers developed a rapid, easy, and reliable way of non-destructive detection of the influence of cold storage on mango. After low temperature preservation, the suggested approach may efficiently differentiate individual fruits.(Hashim et al., 2018).

5.9 Obstacle detection

In a previous study (Steen et al., 2016) looked at a CaffeNet-based AlexNet framework for identifying obstacles, which had a high classification efficiency of 99.9% in row crops and 90.8% in grass mowing. The research focuses on finding ISO barrel-shaped barriers in row crops and grassland mowing by utilizing 437 photos as a dataset to obtain the framework. Another work (Christiansen et al., 2016) proposed an obstacle detection model based on AlexNet and VGG assisted by CaffeNet with a 0.72 F1 score.

Irrigation monitoring system

Irrigation monitoring techniques assist farmers by minimizing monthly irrigation expenditures and restricted water resources through the installation of different sensing devices (Keswani et al., 2018). Researchers (Hellin et al., 2014) presented a more broad, sophisticated method that employs cellular technology to regulate the irrigation operation. Sensor data may be sent to the system database utilizing mobile technology in the suggested technique. One research (Mohanraj et al., 2016) proposed a framework for field monitoring and automation utilizing IoT in agriculture, consisting of KM-knowledge base and tracking modules. A knowledge-based data flow model was built to connect different sources to crop structures, and an analysis of the development system and the current setup was shown. The technology overcomes the limits of conventional agricultural techniques by efficiently using water resources and lowering labor costs.

In one of the recent study (Ikhwan & Thamrin, 2017), scholars presented an IoT paradigm based on sensor nodes for leveraging wireless communication to evaluate physithe cal and chemical limits of water, such as the pH level, temperature, oxygen, and conductivity. Cloud-based services were used to monitor the collected database regarding the water control system on the Internet. The suggested system also regulates field water usage. Another study (Nawandar & Satpute, 2019) designed and created a low-cost irrigation system based on IoT including HTTP and MQTT protocol compatibility. The suggested system's outcomes, with their intelligence, mobility, and low expenses, promise to be advantageous.

6.6 Optimum time for plant and harvesting

Research (Kamilaris et al., 2016) offered an IoT-based system for data collecting, processing, and analyzing in real time. This would deliver real-time provisioning or smart solutions, as well as expert decision assistance to researchers and farmers. Furthermore, by utilizing fewer resources such as water, fertilizer, and so on, this smart agriculture framework boosts production while protecting the environment.

6.7 Tracking and tracing

One research (Satyanarayana, 2013) invented a model that monitors soil status using the ZigBee network and other devices including GPRS, CMS, and GPS. However, the suggested strategy is costly yet widely used in agriculture because of its precise position monitoring and tracking capabilities. Another research (Farooq et al., 2019) offered a framework for IoT-enabled agriculture solutions. The author also discussed network technologies such as network architecture and layers, as well as the connectivity of an IoT-based farm system to essential technologies.

6.8 Farm management system

A farm management system serves as crucial for smart agricultural processing, planning, and making decisions (Gardasevic et al., 2017). One research (Elijah et al., 2018) looked at how IoT may be used with data analytics to enable smart agriculture. The author categorized all of the benefits and obstacles of using IoT in the agriculture industry. The primary goal is to raise awareness of research in the design and development of LPWA communications. Furthermore, as the cost of IoT devices, data storage, processing, and transport decreases over time, small and medium-sized farms will be able to install IoT systems.

6.9 Agricultural drone

UAVs, or agricultural drones, are utilized to enhance various farming methods and processes. Selection, scouting reports, crop health evaluation, nitrogen measuring, spraying, and soil condition monitoring are all agricultural procedures. A recent research (Bodake et al., 2018) developed a system for mapping and capturing crop health images using drones that is based on the combination of IoT and GIS. The suggested technology is designed specifically for tracking bacteria and fungi on farms.

7 Role of wireless sensor networks in agriculture

WSN technologies are available for sensing and evaluating the many parameters necessary in agriculture. Many applications have been developed to use sensors in agriculture. Sensor networks are the finest possibilities for establishing a strong connection between cyberspace and the physical world. Sensors are designed to link agriculture to the Internet of Things. WSN are low-cost devices that can operate in certain settings for lengthy periods of time without requiring battery replacement (Louis & Dunston, 2018). The notion of precision farming is defined, and important parts of precision and smart farming are investigated. In one research (Yanxia et al., 2007), the notion of GIS, a unique information system, is examined in depth. The system combines GIS methodologies, agro-techniques, scientific research findings, expert expertise, and computer technology to create a comprehensive precision farming expert system with high intelligence. This section examines the advancements in image processing in agriculture and food processing.

7.3 Precision farming

One research (Bencini et al., 2012) developed a feasible solution for agro-food chain tracking and supervision through design, optimization, and development. VineSense's primary characteristics have been discussed. Furthermore, several significant agronomic outcomes obtained through the application of VineSense in various scenarios were sketched out, underlining the good benefits of WSN technology for the agricultural environment. Another research (Piyare&Lee, 2013) presented an extensible and adaptable architecture for integrity WSN with cloud computing for data gathering and sharing using REST-based web-based services. The test shows that consumers may access the data from any location and on any mobile device with internet connectivity. This proposed methodology is an energy-efficient solution for extending the lifespan of sensory nodes. In a different research (Bhanu et al., 2014), an agricultural monitoring system was created and built to decrease manual labor. This technology measures the parameters and relays the results to farmers. Even tiny changes in parameters are detected.

With the continuous monitoring of numerous environmental indicators, the WNS system design and data architecture were addressed; the producer may assess the best environmental conditions for attaining maximum crop productivity and amazing energy savings. According to one study (Gangurde & Bhende, 2015), the WSN is a game changer in the field of precision agriculture. The suggested WSN system has the potential to regulate agricultural factors and boost growth. In one recent research (Jawad et al., 2017) offered a comparison of several wireless technologies or protocols and recommended a system that employs the ZigBee and Lora wireless protocols, which are useful due to their low power consumption and long communication range. A categorization of energy-efficient approaches algorithm, as well as energy harvesting and techniques, was also introduced. Another research (Siva Rama Krishnan & Arun Kumar, 2019) proposed an approach for smart agricultural practical implementation utilizing WSN-recommended routing. The data is collected and transferred by an RF transmitter to a single server, which analyses the data and generates further details. The authors offer a method for controlling specific parameters in order to make the most use of available resources.

9 Conclusion

In the future decades, farming will be more important than ever. Smart agriculture and precise agriculture are only getting started, but they might pave the way for far larger use of technology in the farming environment. Smart farming is intended to bridge the gap between farmers in developing and developed countries. Technological advancement, IoT development, and mobile application have all contributed considerably to the acceptability of technology in agriculture. It's no surprise that most traditionally performed agricultural activities have changed drastically. Technical progress can be related to smart farming approaches and methodologies such as the use of computers, software, sensors, and information technology. Evidently, smart farming is an intelligent agricultural concept that, when correctly implemented, may help farmers gain a variety of benefits, including higher output, improved quality, and lower expenses. Such innovative thinking requires the use of resources, knowledge, and technical abilities. You need more than simply a passion for farming to assess your farm's data, account for and follow advancements, and forecast demand and price fluctuations. This chapter seeks to offer a concise summary to agricultural and smart farming researchers. Almost all peer-reviewed quality publications over the previous years were examined. Because each publication examined uses a unique collection of datasets, metrics, preprocessing methods, models, and parameters, it is impossible to generalize and compare the articles. The final line is that, while smart farming is important in agriculture and promises higher yields, study on best practices that meet your agricultural goals and needs is recommended.

Reference

- Ali, I., Cawkwell, F., Dwyer, E., & Green, S. (2016). Modeling managed grassland biomass estimation by using multitemporal remote sensing data—A machine learning approach (pp. 1–16).

- Amatya, S., Karkee, M., Gongal, A., & Zhang, Q. (2015). ScienceDirect detection of cherry tree branches with full foliage in planar architecture for automated sweet-cherry harvesting. Biosystems Engineering, 1–13.

- Anonymous (2014).Country presentation paper, Agricultural Machinery Manufacturers Association (AMMA) India, October 2014

- Aravind, K. R., Raja, P., & P_erez-ruiz, M. (2017). Task-based agricultural mobile robots in arable farming : A review. Spanish Journal of Agricultural Research, 15, 1–16.

- Badrinarayanan, V., Kendall, A., & Cipolla, R. (2017). SegNet: A deep convolutional encoder-decoder architecture for image segmentation. IEEE Transactions on Pattern Analysis and Machine Intelligence, 39, 2481–2495.

- Bhabad, A. R., Puranik, G. S., Sonawane, I. S., Pawar, M. R., & Mali, A. R. (2017). Design and Fabrication of Agricultural Crops Reaper. International Journal For Research In Applied Science & Engineering Technology (IJRASET), 5: 1438-1442.

- Bogue, R. (2016). Robots poised to revolutionise agriculture. Industrial Robot: An International Journal Iss An International Journal, 32, 468–471.

- Bosilj, P., Duckett, T.,&Cielniak, G. (2018). Connected attribute morphology for unified vegetation segmentation and classification in precision agriculture. Computers in Industry, 98, 226–240.

- Botta A, De Donato W, Persico V, Pescapé A. Integration of cloud computing and Internet of Things: A survey. Future Gener Comput Syst 2016; 56: 684-700. [http://dx.doi.org/10.1016/j.future.2015.09.021]

- Butz, P., Hofmann, C., & Tauscher, B. (2006). Recent developments in noninvasive techniques for fresh fruit and vegetable internal quality analysis. Journal of Food Science, 70, R131–R141.

- Chahal, N., & Anuradha. (2015). A study on agricultural image processing along with classification model. In 2015. Souvenir of the 2015 IEEE international advance computing conference, IACC (pp. 942–947).

- Chung, C., Huang, K., Chen, S., Lai, M., Chen, Y., & Kuo, Y. (2016). Detecting Bakanae disease in rice seedlings by machine vision. Computers and Electronics in Agriculture, 121, 404–411.

- Coopersmith, E. J., Minsker, B. S., Wenzel, C. E.,&Gilmore, B. J. (2014). Machine learning assessments of soil drying for agricultural planning. Computers and Electronics in Agriculture, 104, 93–104.

- Costa, C., Antonucci, F., Pallottino, F., Aguzzi, J., Sun, D. W., & Menesatti, P. (2011). Shape analysis of agricultural products: A review of recent research advances and potential application to computer vision. Food and Bioprocess Technology, 4, 673–692.

- D. D. Wu, D. L. Olson, and J. R. Birge, “Risk management in cleaner production,” J. Clean. Prod., vol. 53, pp. 1-6, 2013.

- Dahikar SS, Rode SV. Agricultural crop yield prediction using artificial neural network approach. Int J Innovative Res Electr Electron Instrum Control Eng 2014; 2(1): 683-6.

- Farmer, M. E., & Jain, A. K. (2005). A wrapper-based approach to image segmentation and classification. IEEE Transactions on Image Processing, 14, 2060–2072.

- Femat-Diaz, A., Vargas-Vazquez, D., Huerta-Manzanilla, E., Rico-Garcia, E., & Herrera-Ruiz, G. (2011). Scanner image methodology (SIM) to measure dimensions of leaves for agronomical applications. African Journal of Biotechnology, 10, 1840–1847.

- Feng, C.-H., Makino, Y., Yoshimura, M., Thuyet, D. Q., & Garcı´a-Martı´n, J. F. (2018). Hyperspectral imaging in tandem with R statistics and image processing for detection and visualization of pH in Japanese big sausages under different storage conditions. Journal of Food Science, 83, 358–366.

- Freixenet, J., Mun˜oz, X., Raba, D., Martı´, J., & Cufı´, X. (2002). Yet another survey on image segmentation:

- Gao, H., Zhu, F., & Cai, J. (2010). A review of non-destructive detection for fruit quality. IFIP Advances in Information and Communication Technology, 317, 133–140.

- Ghosal, S., Blystone, D., Singh, A. K., Ganapathysubramanian, B., Singh, A., & Sarkar, S. (2018). An explainable deep machine vision framework for plant stress phenotyping. Proceedings of the National Academy of Sciences of the United States of America, 115, 4613–4618.

- Gonzalez Viejo, C., Fuentes, S., Torrico, D. D., Howell, K.,& Dunshea, F. R. (2018). Assessment of beer quality based on a robotic pourer, computer vision, and machine learning algorithms using commercial beers. Journal of Food Science, 83, 1381–1388.

- Hani, N., Roy, P., & Isler, V. (2018). Apple counting using convolutional neural networks. In IEEE international conference on intelligent robots and systems (pp. 2559–2565).

- Hashim, N., Onwude, D. I., & Osman, M. S. (2018). Evaluation of chilling injury in mangoes using multispectral imaging. Journal of Food Science, 83, 1271–1279.

- Hu, H., Pan, L., Sun, K., Tu, S., Sun, Y., Wei, Y., & Tu, K. (2017). Differentiation of deciduous-calyx and persistent-calyx pears using hyperspectral reflectance imaging and multivariate analysis. Computers and Electronics in Agriculture, 137, 150–156.

- Jeschke S, Brecher C, Meisen T, Özdemir D, Eschert T. Industrial Internet of Things and Cyber Manufacturing Systems.Industrial Internet of Things. Cham: Springer 2017; pp. 3-19. [http://dx.doi.org/10.1007/978-3-319-42559-7_1]

- Jha, K., Doshi, A., Patel, P., & Shah, M. (2019). Arti fi cial intelligence in agriculture a comprehensive review on automation in agriculture using artificial intelligence. Artificial Intelligence in Agriculture, 2, 1–12.

- Jhuria, M., Kumar, A.,&Borse, R. (2013). Image processing for smart farming: Detection of disease and fruit grading. In 2013 IEEE 2nd international conference on image information processing (pp. 521–526). IEEE ICIIP.

- Johann, A. L., De Arau´ jo, A. G., Delalibera, H. C., & Hirakawa, A. R. (2016). Soil moisture modelling based on stochastic behavior of forces on a no-till chisel opener. Computers and Electronics in Agriculture, 121, 420–428.

- Kamilaris, A., Gao, F., Boldu, P., Francesc, X., & Intizar Ali, M. (2016). Agri-IoT : A semantic framework for internet of things-enabled smart farming applications. In IEEE 3rd world forum on internet of things (WF-IoT).

- Keller, M., Rosenberg, M., Brettel, M., & Friederichsen, N. (2014). How virtualization, Decentrazliation and network building change the manufacturing landscape: An industry 4.0 perspective. International Journal of Mechanical, Aerospace, Industrial Mechatronic and Manufacturing Engineering, 8, 37–44.

- Kung, H., Kuo, T., Chen, C., & Tsai, P. (2016). Accuracy analysis mechanism for agriculture data using the ensemble neural network method. In Sustainability (pp. 1–11). MDPI.

- Kussul, N., Lavreniuk, M., Skakun, S., & Shelestov, A. (2017). Deep learning classification of land cover and. IEEE Geoscience and Remote Sensing Letters, 14, 778–782.

- Kuwata, K., & Shibasaki, R. (2015). Estimating crop yields with deep learning and remotely sensed data. In IEEE international geoscience and remote sensing symposium (IGARSS) (pp. 858–861).

- Lakhwani K, Gianey H, Agarwal N, Gupta S. Proceedings of the Emerging Trends in Expert Applications and Security (ICETEAS 2018). Jaipur, India. Singapore: Springer 2019; pp. February 17-18, 2018; 425-32.

- Lamb, D. W., & Brown, R. B. (2001). Remote-sensing and mapping of weeds in crops. Journal of Agricultural and Engineering Research, 78, 117–125.

- Liakos, K. G., Busato, P., Moshou, D., & Pearson, S. (2018). Machine learning in agriculture: A review. Sensors, 1–29.

- Ma J, Zhou X, Li S, Li Z. In: Connecting agriculture to the Internet of Things through sensor networks, Proceedings of the 2011 International Conference on Internet of things and 4th International Conference on Cyber, Physical and Social Computing, Dalian,. China. 2012; pp. October 19-22, 2011; IEEE; 184-7.

- Maione, C., Lemos, B., Dobal, A., Barbosa, F., & Melgac¸o, R. (2016). Classification of geographic origin of rice by data mining and inductively coupled plasma mass spectrometry. Computer and Electronics in Agriculture, 121, 101–107.

- Mendoza, F., & Aguilera, J. M. (2004). Application of image analysis for classification of ripening bananas. Journal of Food Science, 69, 471–477.

- Morellos, A., Pantazi, X., Moshou, D., Alexandridis, T., Whetton, R., Tziotzios, G.,…Mouazen, A. M. (2016). ScienceDirect special issue : Proximal soil sensing machine learning based prediction of soil total nitrogen, organic carbon and moisture content by using VIS-NIR spectroscopy. Biosystems Engineering, 1–13.

- Moshou, D., Bravo, C., Oberti, R., West, J., Bodria, L., Mccartney, A., & Ramon, H. (2005). Plant disease detection based on data fusion of hyper-spectral and multi-spectral fluorescence imaging using Kohonen maps. Real-Time Imaging, 11, 75–83.

- Moshou, D., Pantazi, X., & Kateris, D. (2013). Water stress detection based on optical multisensory fusion with a least squares support vector machine classifier 5. Biosystems Engineering, 117, 15–22.

- Murugesan, R., Sudarsanam, S. K., Malathi, G., Vijayakumar, V., Neelanarayanan, V., Venugopal, R., … Malolan, V. (2019). Artificial intelligence and agriculture 5. 0. International Journal of Recent Technology and Engineering (IJRTE) ISSN:2277-3878, 8, 1870–1877.

- Nahvi, B., Habibi, J., Mohammadi, K., & Shamshirband, S. (2016). Using self-adaptive evolutionary algorithm to improve the performance of an extreme learning machine for estimating soil temperature. Computers and Electronics in Agriculture, 124, 150–160.

- Pandey, Chanki & Sethy, Prabira & Santi, Kumari & Vishwakarma, Jaya & Tande, Vishal. (2022). Smart agriculture: Technological advancements on agriculture- A systematical review. 10.1016/B978-0-323-85214-2.00002-1.

- Pantazi, X. E., Moshou, D., & Bochtis, D. (2017). Detection of biotic and abiotic stresses in crops by using hierarchical self organizing classifiers. Precision Agriculture.

- Pantazi, X. E., Moshou, D., Alexandridis, T., Whetton, R. L., & Mouazen, A. M. (2016). Wheat yield prediction using machine learning and advanced sensing techniques. Computers and Electronics in Agriculture, 121, 57–65.

- Pantazi, X. E., Moshou, D., Alexandridis, T., Whetton, R. L., & Mouazen, A. M. (2016). Wheat yield prediction using machine learning and advanced sensing techniques. Computers and Electronics in Agriculture, 121, 57–65.

- Patrício D, Rieder R. Computer vision and artificial intelligence in precision agriculture for grain crops: A systematic review. Computer Electron Agric 2018; 153: 69-81.

- Pedersen, & Kjeldgaard, S. J. (2007). Circular Hough transform. Aalborg University, Vision, Graphics, and Interactive Systems, 123(6), 181.

- Poojith, A., Reddy, B. V. A., & Kumar, G. V. (2014). Image processing in agriculture. International Journal of Innovative Research in Electrical, Electronics, Instrumentation and Control Engineering, 2, 207–230.

- Prabha, D. S., & Kumar, J. S. (2013). Three dimensional object detection and classification methods: A study. International Journal of Engineering Research and Science & Technology, 2, 33–42.

- Prakash, K., Saravanamoorthi, P., Sathishkumar, R., & Parimala, M. (2017). A study of image processing in agriculture. Int. J. Advanced Networking and Applications, 22, 3311–3315.

- Ramos, P. J., Prieto, F. A., Montoya, E. C.,&Oliveros, C. E. (2017). Automatic fruit count on coffee branches using computer vision. Computers and Electronics in Agriculture, 137, 9–22.

- Region and boundary information integration. Lecture Notes in Computer Science (including subseries Lecture Notes in Artificial Intelligence and Lecture Notes in Bioinformatics), 2352, 408–422.

- Reiser D, Sehsah ES, Bumann O, Morhard J, Griepentrog HW. Development of an autonomous electric robot implement for intra-row weeding in vineyards. Agric 2019; 9(1): 18.

- Saiz-Rubio, V., & Rovira-Ma´s, F. (2020). From smart farming towards agriculture 5.0: A review on crop data management. Agronomy, 10.

- Sarkar, A. (2020). Agricultural mechanization in India: a study on the ownership and investment in farm machinery by cultivator households across agro-ecological regions. Millennial Asia, 11(2): 160-186.

- Surya, P., & Satheesh, K. (2014). Image processing methods and its role in agricultural sector—A study. International Journal of Business Intelligents, 03, 366–373.

- Tewari, V. K., Pareek, C. M., Lal, G., Dhruw, L. K., & Singh, N. (2020). Image processing based real-time variable rate chemical spraying system for disease control in paddy crop. (Artificial Intelligence in Agriculture).

- Ying-xue, S., Huan, X., & Li-jiao, Y. (2017). Support vector machine-based open crop model (SBOCM ): Case of rice production in China. Saudi Journal of Biological Sciences, 24, 537–547.